## Slide 1: Rear End Service Honda Valkyrie
Plus Changing Drive Dampeners

## Slide 2: Lift with Wood Adapter
Engage safety

## Slide 3: Remove seat, Tie Down

## Slide 4: Remove Right Side Shock The four bolt to remove the final drive are easy to access with the shock removed
4 bolts to remove final drive

## Slide 5: Remove left side shock/Replace with solid short bar (substitute a tie down strap…lower shock mount to sissy bar)
Now the axle is above the exhausts so you don’t have to mess with exhaust at all
Caliper plate holding pin

## Slide 6: Remove the Caliper holding pin, axle nut & axle, then slide the caliper off the rotor and tie it up
I use a bungee cord to keep tension off the hydraulic line and the caliper out of the way

## Slide 7: Remove the wheel

## Slide 8: Splines are great Now remove the four final drive bolts and remove the drive train

## Slide 9: Parts all cleaned up
New 0-rings and Thrust washer

## Slide 10: Remove Flange, Dampener Plate and Dampeners

## Slide 11: Install new Dampeners “outside” Out
They fit much better after sleeping in the freezer all night

## Slide 12: Line up the arrow and line

## Slide 13: Turn the plate so the tabs go in the grooves locking the dampners in

## Slide 14: Blue locktite and bolt the plate in

## Slide 15: Light grease on the Thrust washer and put on the new O-Ring
Thrust Washer sitting on top of the hub

## Slide 16: Light Grease on the Flange/New Big O-Ring

## Slide 17: Wheel all ready for Installation

## Slide 18: The Elusive Third O-Ring

## Slide 19: After cleaning the old grease out…put new grease in the female side of the splines. Light coat of Moly (Guard Dog) and then Lucas Grease

## Slide 20: Pinion Cup and Drive Shaft are good

## Slide 21: Drain the Final Drive

## Slide 22: Fill with Hypoid Gear Oil (150cc)

## Slide 23: Grease is Lucas Heavy Duty/ Oil is Lucas Synthetic

## Slide 24: Make sure its Hypoid Rated

## Slide 25: Lightly grease the Drive shaft (both ends) and put it back into the pinion cup
Snaps right in

## Slide 26: Install the drive train…..Hold the final drive and just find the U-Joint with the driveshaft and its done

## Slide 27: Finger Tight Only on the four bolts holding the Final Drive

## Slide 28: Lift Wheel in place

## Slide 29: Now the BIG important three steps after the axle is through the final drive, wheel, spacer, caliper plate and swing arm…
1. Rotate the caliper plate into position and install the pin (bolt) that plate sure isin’t going to move after you torque the axle.
2. Torque the axle to 81ftlbs while the final drive is loose and free and the 4 bolts are only finger tight
3. Torque the 4 Final Drive Bolts to 47ftlbs and now you have a properly aligned rear end.

## Slide 30: Installing the right side lower shock bolt and the caliper plate holding pin
These are both “pins” they just go through a hole to block movement. They will not hold any better if you over tighten them. Use anti seize on the threads of both of them (especially the shock bolt because its steel into aluminum) and snug them up about as tight as a spark plug
Right side lower shock bolt
Caliper plate holding bolt (pin)

## Slide 31: Put the Shocks back on and you are ready to ride